## Slide 1: POWER PLANTS
Module 3

## Slide 2: POWER PLANTS
A power plant is an industrial facility used to generate electric power with the help of one or more generators which converts different energy sources into electric power.
Electricity is a secondary energy source - obtained from the conversion of other primary sources of energy :- coal, natural gas, nuclear, solar, hydraulic or wind energy.
Electricity itself is neither renewable nor non-renewable.
The power plant is the location in which the energy conversions take place.

## Slide 3: Conventional Power Plants
Fossil fuel power plants: Generates electric power by burning fossil fuels like coal, natural gas or diesel.
Nuclear power plants: Controlled nuclear reaction is maintained to generate electricity.
Hydroelectric power plants: Electricity is produced by building dams on suitable rivers.

## Slide 4: Non-Conventional Power Plants
Wind power plants: The kinetic energy of wind is used to create power.
Solar power plants: Generates power by collecting solar radiation.
Geothermal power plants: Uses the natural heat found in the deep levels of the earth to generate electricity.
Biomass power plants: Natural organic matter is burnt to produce electricity.

## Slide 5: Power Plants
Hydro-electric power plants
Thermal power plants
Nuclear power plants
Diesel power plants
Wind power plants
Solar power plants

## Slide 6: Hydro - electric Power Plants
Hydro energy:- Energy generated by the force of water.
Production of electricity depends upon:-
                Water level from the ground
                Flow rate of water
                Efficiency of turbine

## Slide 7: Hydro-electric Power Plants

## Slide 8: Hydro-electric Power Plants
Advantages
      The most important advantage is that it keeps the environment clean
      Hydro energy can be stored in high level reservoirs and used whenever necessary.
      Electricity is produced at a constant rate.
      The life of dams and power plants last for many decades.
      The water can be used for supplying
                Drinking water
                Irrigation
                Water sports
                Industries
                Power plants

## Slide 9: Hydro-electric Power Plants
Disadvantages
      Constructing hydroelectric power plants and dams are very expensive.
      Requires large area.
      Planning a hydro electric power plant and reservoir may lead to the disruption of the lives of people as they have to relocate to another area.

## Slide 10: Thermal Power Plants
A generating station which converts heat energy of coal combustion into electrical energy is known as a steam power station
The heat produced for burning of coal & with the help of water steam is produced. This produced steam flow towards turbine i.e. kinetic energy of the steam which converted into mechanical energy of the turbine. The input steam drives the prime mover or turbine, simultaneously the generator also start to rotate. At that time mechanical energy is converted into electrical energy.
Rankine cycle

## Slide 11: Thermal Power Plants

## Slide 12: Thermal Power Plants
Advantages:
      Less initial cost as compared to other generating stations.
      It requires less land as compared to hydro power plant.
      The fuel (i.e. coal) is cheaper.
      The cost of generation is lesser than that of diesel power plants.

## Slide 13: Thermal Power Plants
Disadvantages:
      It pollutes the atmosphere due to the production of large amount of smoke. This is one of the causes of global warming.
      The overall efficiency of a thermal power station is low (less than 30%).

## Slide 14: Nuclear Power Plants
Nuclear power plants generate electricity in a very similar way to other traditional power plants, differing in the type of fuel used. All electricity generation plants produce heat that turns water into steam, which drives a turbine connected to a generator and subsequently produces electricity.
In a nuclear reactor, uranium atoms are split into smaller parts by changing their molecular structure using the fission process. The energy released during this split creates heat to produce steam, which is used by a turbine generator to generate electricity.

## Slide 15: Nuclear Power Plants

## Slide 16: Nuclear Power Plants
Advantages
      Produces no polluting gases.
      Does not contribute to global warming.
      Low fuel quantity reduces mining and transportation effects on environment.
      Power station has very long lifetime.

## Slide 17: Nuclear Power Plants
Disadvantages
      Waste is radioactive and safe disposal is very difficult and expensive.
      Costs of building and safely decommissioning are very high.
      Cannot react quickly to changes in electricity demand.
      Local thermal pollution from wastewater affects marine life.

## Slide 18: Diesel Power Plants
A Diesel power station (also known as Stand-by power station) uses a diesel engine as prime mover for the generation of electrical energy. This kind of power station can be used to produce limited amounts of electrical energy.
The diesel burns inside the engine and the products of this combustion act as the working fluid to produce mechanical energy. The diesel engine drives alternator which converts mechanical energy into electrical energy

## Slide 19: Diesel Power Plants

## Slide 20: Diesel Power Plants
Advantages
      Quick installation and commission
      Quick starting and easy pick-up of loads
      Easy operation
      Required minimum labours
      Simple fuel handling
      Efficient ash disposal
      High level of efficiency

## Slide 21: Diesel Power Plants
Disadvantages
      Limited power generation capacity.
      Expensive due to the use of diesel.
      High maintenance cost.
      Relatively short life.

## Slide 22: Wind Power Plants
Wind turbines operate on a simple principle. The energy in the wind turns two or three propeller-like blades around a rotor. The rotor is connected to the main shaft, which spins a generator to create electricity

## Slide 23: Wind Power Plants
Wind Power Plant.mp4

## Slide 24: Wind Power Plants
Advantages
      Clean & Environment friendly Fuel source
      Renewable & Sustainable
      Cost Effective
      Industrial and Domestic Installation

## Slide 25: Wind Power Plants
Disadvantages
      Fluctuation of Wind and Good wind sites
      Noise and aesthetic pollution
      Not a profitable use of land

## Slide 26: Solar Power Plants
A solar power plant is any type of facility that converts sunlight either directly, like Photovoltaics, or indirectly, like Solar Thermal plants, into electricity.
Photovoltaics
When photons from sunlight hit the semiconductor material free electrons are generated which can then flow through the material to produce a direct electrical current - known as the photo - effect in physics.
DC to AC - convertors
Can use the photo-effect directly without the need of other processes or devices.
Photovoltaic.mp4

## Slide 27: Solar Power Plants
Solar Thermal Power Plants
These kinds of solar thermal power plant work by focusing sunlight from long parabolic mirrors onto receiver tubes that run the length of the mirror at their focal point. This concentrated solar energy heats up a fluid that continuously flows through the tubes.
This heated fluid is then sent to a heat exchanger to boil water in a conventional steam-turbine generator to generate electricity.
Solar Thermal Power plant.mp4

## Slide 28: Solar Power Plants
Advantages
      Renewable Energy Source
      Reduces Electricity cost
      Diverse Applications
      Low Maintenance Costs
      Technology Development

## Slide 29: Solar Power Plants
Disadvantages
      Weather Dependent
      Solar Energy Storage is Expensive
      Uses a Lot of Space
      Associated with Pollution